# Team
## B00125142 Violet Concordia
## Bernardo Borile
## Kevin
## Farouk
# Introduction
## A 75% duty cycle LED blinking program, running on an FPGA board.
# Specifications
## Clock freq
### 66MHz
### Operations per second 33M
## Frequency
### 2Hz
## Duty cycle
### 75%
## Off cycle
### 25%
#### 100% - Duty cycle
##### 100% - 75% = 25%
# Calculations
## Discussion
### To achieve delay, a loop will be used to keep the processor busy for a specific amount of time.
### PicoBlaze is 8bit
#### Registers only hold values ranging 0-255
##### 256 different values
###### Therefore we must nest loops to achieve delay higher than 256 computations duration.
##### If we want to loop for a single second, we would need to count up to 33 Million.
##### To circumvent this, nested loops will be utilised, which essentially provide us a way to keep track of up to 256^n per loop, n being the loop count.
###### The calculations below determined that nests of a minimum of 4 depth will be required for both the on and off cycles.
## Duration
### Seconds
#### Total duration per cycle
##### 2s
#### On duration
##### 1.5s
###### Total duration * Duty cycle
#### 2 * 0.75 = 1.5sOff duration
##### 0.5s
###### Total duration - On duration = Off duration
### 2 - 1.5 = 0.5sCycles
#### Total operations per cycle
##### Operations per second * On duration (seconds)
###### 33M * 2 = 66M operations
#### On operations count
##### 49.5M operations
###### Total operations per cycle * Duty cycle
#### 66M * 0.75 = 49.5MOff operations count
##### 16.5M operations
###### Total operations per cycle * Off cycle
# 66M * 0.25 = 16.5MCode
## TypeScript
### Script developed to assist calculations
#### Language
##### TypeScript
#### Constants
##### export const BITS = 8; export const MAX_INT = Math.pow(2, BITS); export const K = 1_000; export const KK = 1_000*K; export const FREQ = 33*KK; export const TOGGLE_FREQ = 2; export const TOGGLE_CYCLES = 2*FREQ; export const DUTY_CYCLE = 0.75; export const ON_TIME_S = TOGGLE_FREQ*DUTY_CYCLE; export const ON_CYCLES = ON_TIME_S*FREQ; export const OFF_TIME_S = TOGGLE_FREQ - ON_TIME_S; export const OFF_CYCLES = OFF_TIME_S*FREQ;
#### Functions
##### findBiggestDivider
###### /** * author: B00125142 Violet Concordia * Brute force approach to find the highest divider without remainder * * @param input the number to divide * @returns the divider without remainder */ export function findBiggestDivider(input: number, max: number = MAX_INT): number { //Decrement loop `max` until either a no remainder result is found, or it reaches 0. for(; max > 0; --max) { if(input/max % 1 == 0) break; } //Return max, which is hopefully the highest number without a remainder. (Worst case scenario, it is 0) return max; }
##### findBiggestDividers
###### /** * author: B00125142 Violet Concordia * Appends every highest no remainder divider to an array, until the input number is below the `max` value. * * @param input The number to divide. * @returns The dividers array. */ export function findBiggestDividers(input: number, max: number = MAX_INT): number[] { //Init array that will be returned. const dividers = []; //While input is higher than max number while(input >= max) { //Find biggest no remainder divider. const biggestDivider = findBiggestDivider(input, max); //Push the found value. dividers.push(biggestDivider); // console.log(`${input} / ${biggestDivider} = ${input / biggestDivider}`); //Divide by found value. input = input / biggestDivider; } //Push the remainder to result in a 1. dividers.push(input); //Return the dividers. return dividers; }
#### Results
##### Finding highest dividers
###### Code
###### console.log(`1s = ${FREQ} instructions`); console.log(`On for ${ON_TIME_S}s, Off for ${OFF_TIME_S}s, total: ${TOGGLE_FREQ}s`); console.log(`On for ${ON_CYCLES} cycles, Off for ${OFF_CYCLES} cycles, total: ${TOGGLE_CYCLES} cycles`); const onDividers = findBiggestDividers(ON_CYCLES); console.log(`${("" + onDividers).replace(/,/g, " * ")} = ${ON_CYCLES}`); const offDividers = findBiggestDividers(OFF_CYCLES); console.log(`${("" + offDividers).replace(/,/g, " * ")} = ${OFF_CYCLES}`);Output
##### RawDebugger attached. 1s = 33000000 instructions On for 1.5s, Off for 0.5s, total: 2s On for 49500000 cycles, Off for 16500000 cycles, total: 66000000 cycles 49500000 / 250 = 198000 198000 / 250 = 792 792 / 198 = 4 250 * 250 * 198 * 4 = 49500000 16500000 / 250 = 66000 66000 / 250 = 264 264 / 132 = 2 250 * 250 * 132 * 2 = 16500000 Waiting for the debugger to disconnect... harmony@harmony:/media/2TB_Crucial_SSD/repos/ratios/freq_calc$InformationOn dividers250 * 250 * 198 * 4 = 49500000Off dividers250 * 250 * 132 * 2 = 16500000Both the off and on delays can be achieved by a minimum of 4 nested loop.Example in JavaScript of what will be translated to assembly code for the PicoBlaze
###### Variables
###### onDividers = [250, 250, 198, 4]Code
###### let count = 0; for(let i0 = onDividers[0]; i0 > 0; --i0) { for(let i1 = onDividers[1]; i1 > 0; --i1) { for(let i2 = onDividers[2]; i2 > 0; --i2) { for(let i3 = onDividers[3]; i3 > 0; --i3) { ++count; } } } } console.log(count);Output
## 49500000As expected, the obtained dividers from the previous script have resulted in a nested loop of 49500000 operations, which is the amount we need to wait exactly 1.5 seconds, which is the on time for a duty cycle of 75% of 2 seconds.Assembly
## Vivado